## Slide 1
MoveWell
AI-Powered Computer Vision Workout & Rehabilitation
Real-time exercise posture assessment • quality-aware repetition counting • remote clinician monitoring
COMPUTER VISION
01

## Slide 2
The Problem
Why home-based rehabilitation needs more than a repetition counter
Incorrect exercise form
Patients often perform prescribed movements without real-time posture correction.
Quantity over quality
Conventional workout apps can count movement but may not validate whether the repetition was performed correctly.
Limited clinician visibility
Physiotherapists cannot continuously observe patients between in-person visits.
Manual follow-ups
Progress tracking and follow-up can become time-consuming and inconsistent.
Goal: detect movement in real time → validate posture → give instant feedback → track rehabilitation remotely
02

## Slide 3
The MoveWell Solution
One platform connecting the patient, computer vision engine and physiotherapist
PATIENT
Camera-based workout
AI ENGINE
Pose → angles → exercise state → form quality
CLINICIAN
Plans, reports & review
Real-time guidance
The patient receives immediate visual and voice corrections.
Quality-aware reps
Only repetitions satisfying configured movement criteria are counted as valid.
Remote monitoring
Session data becomes part of the patient's progress history.
03

## Slide 4
How the AI Workout Works
The core MoveWell pipeline
1
Webcam
Live camera feed
2
Pose
33 body landmarks
3
Geometry
Joint angles
4
FSM
Movement phases
5
Quality
Correct / incorrect
6
Feedback
Reps + guidance
Key principle
The system does not ask only “Did the user move?” It asks whether the required movement was completed with the required biomechanical quality.
04

## Slide 5
Real-Time Body Tracking
MediaPipe Pose Landmarker traces the user's movement through anatomical landmarks
33 body landmarks
The pose model extracts landmarks across the head, shoulders, elbows, wrists, hips, knees, ankles and feet.
Skeleton overlay
A transparent Canvas layer connects landmarks so the visual skeleton follows the user's body in real time.
Confidence-aware tracking
If key landmarks are not visible or confidence is too low, the system pauses assessment instead of producing misleading measurements.
05

## Slide 6
Example: Intelligent Squat Assessment
A repetition is counted only after the required movement cycle and quality checks
Knee angle → 96°
STANDING
Ready
DESCENDING
Angle decreases
BOTTOM
≤ 100°
ASCENDING
Returning
VALID REP
+1
Quality checks
Depth must be reached, torso alignment must remain within the configured threshold, and the user must return to standing before the repetition is counted.
If correct
VALID REP +1
If incorrect
Feedback + invalid attempt
06

## Slide 7
Real-Time Feedback
The system responds to actual movement quality, not pre-filled messages
Good movement
✓ Correct depth ✓ Acceptable posture → Count repetition
Insufficient depth
⚠ “Squat lower for full depth.” → Do not count as valid
Excessive lean
⚠ “Keep your chest upright.” → Record form issue
Session Form Flaws Log
The workout stores observable problems such as incomplete depth or excessive torso lean so the session summary can show where technique broke down.
Voice + visual guidance
Web Speech API can announce corrections, while the interface shows the current phase, angle, feedback state and repetition count.
07

## Slide 8
Patient Experience
From assigned plan to measurable rehabilitation progress
PLAN
Clinician assigns exercises
WORKOUT
Live camera + AI
SUMMARY
Session metrics
PROGRESS
Trends
Dashboard
Recovery stage, assigned exercises, valid reps, form accuracy, adherence and clinician recommendations.
Session history
Duration, valid/invalid repetitions, accuracy and review status.
Analytics
Form-accuracy trends and valid vs. invalid repetition history.
Outcome
The patient gets immediate guidance during the exercise and longitudinal visibility after the session.
08

## Slide 9
Physiotherapist Portal
Turning workout data into remote rehabilitation oversight
1. Patient roster
View supervised patients, rehabilitation stage, adherence and latest form accuracy.
2. Prescription builder
Create plans with exercises, sets, reps, schedules and clinician instructions.
3. Patient deep-dive
Review session history, movement flaws and performance trends.
Weekly report
Summarizes adherence, average form accuracy, valid/invalid repetitions and common flaws.
Clinical interaction
Recommendations and appointment/telehealth workflows keep the patient connected to the clinician.
Core benefit
Less reliance on manual follow-up, with structured evidence of home exercise performance.
09

## Slide 10
System Architecture
The website combines a client-side CV engine with a clinical management backend
PATIENT / FRONTEND
React + TypeScript Webcam MediaPipe Pose Landmarker Canvas skeleton Joint-angle calculations Exercise FSM Live feedback Recharts analytics
BACKEND / DATA
FastAPI JWT authentication Pydantic validation SQLAlchemy ORM SQLite for local development PostgreSQL for production Workout sessions Plans Appointments Clinical notes
ML / RESEARCH
UI-PRMD dataset Feature extraction Subject-independent evaluation Random Forest benchmark Future extensions: severity scoring recovery prediction wearables EHR integration
Privacy principle
Process pose data client-side where practical; persist structured session metrics rather than raw webcam video.
10

## Slide 11
Future Scope
Where the platform can evolve beyond the current prototype
01 Personalized AI plans
Adapt rehabilitation plans based on observed progress.
02 Severity & recovery prediction
Use ML to estimate progression from longitudinal movement data.
03 Wearable integration
Combine camera-based assessment with sensor data.
04 Multilingual voice guidance
Make spoken exercise guidance more accessible.
05 EHR integration
Connect structured rehabilitation information with electronic health records.
11

## Slide 12
MoveWell: Quality Over Quantity
MoveWell combines computer vision, biomechanical movement assessment and rehabilitation management into one platform.
The core principle is simple: a repetition should be counted only when the required movement is completed correctly.
Patients receive immediate guidance while physiotherapists gain structured visibility into home-based rehabilitation progress.
REAL CAMERA + REAL POSE TRACKING + REAL FORM ASSESSMENT + REAL PROGRESS
AI-POWERED REHABILITATION
12